## Slide 1: Microprocessors and Microcontrollers

## Slide 2: Needed Softwares
AVR Studio
  https://www.microchip.com/mplab/avr-support/atmel-studio-7
  Atmel Studio 7.0 (build 1931) offline installer
This is the IDE

## Slide 3: Burner
Extreme Burner
  http://extreme-burner-avr.software.informer.com/download/
There is also avrpal
Loads the HEX file into microcontroller

## Slide 4: Needed Equipments
Microcontroller – ATmega32
The AVR Programmer / Loader
  To load your code into the mc

## Slide 5: Writing Code
Create New Project
Select “GCC C Executable Project”
Select path to save the project
  You will later need this path for the hex file
Then select device type
  Search for ATmega 32
Now you can write the program

## Slide 6: Compile the hex code
Finish the program
Select “Build Solution (F7)” from the Build Menu
You will find that a hex file is generated in the Debug folder
The name of the hex file will be the same as your project name

## Slide 7: Load the hex into mc
Run Extreme Burner
Load the hex file into it by “Open” and locate your hex file
From menu select Chip -> ATmega32
Set the microcontroller on the AVR Programmer
Connect the programmer with PC
In extreme Burner select the menu “write” and choose “Flash”

## Slide 8: Connecting ATmega32 with programmer
Following the figure connect the 6 corresponding microcontroller pins with the loader.
Be careful about the orientation of the cable layout. The extended part goes to the right

## Slide 9: Setting mc in the AVR Programmer (Not needed for you)
For the big loaders from TechshopBD
  The upper portion (U) side goes closer to the side with the liver
  There is a push button
  Push it so that the yellow LED is on and the red one is off

## Slide 10: Complete Process of Programming a Microcontroller
Write the code
  In ATMEL Studio, or other IDE
Compile it to a .hex file.
  For ATMEL Studio, you will find the hex on the “Debug” folder in your project

## Slide 11: Complete Process of Programming a Microcontroller
3. Inserting the .hex file into the microcontroller
  Load the hex file into burner
  set the microcontroller on the “AVR Programmer”
  Write
4. Set the microcontroller in the working circuit

## Slide 12
☺