## Slide 1: CSE 313 Operating System
Lecture By: Rezwana Reaz

## Slide 2: Textbooks
Modern Operating Systems
  Andrew S. Tanenbaum
  3rd Edition or Newer

## Slide 3: Modern Computer System
Complex system
  Many H/W components
  Many programs running simultaneously
Each running program
  Executed in the CPU
  Resides in the Memory
  May Interact with several devices

## Slide 4: Modern Computer System
To ensure the correct operation someone needs to
  Understand how all these components work
  Manage them wisely
  Allocate them efficiently
A very challenging task!!!
If application programmer had to consider everything
  No code would ever get written
So, computers are equipped with a special software
  THE OPERATING SYSTEM

## Slide 5: What is an OS?
Operating System is nothing but a software
Placement of OS
Scope of Interaction

## Slide 6: Role of OS
An Extended machine
  Provides application programmers a clean abstract set of resources instead of the messy hardware ones.
    Works as an intermediary between applications/users and hardware
Resource manager
  Manages the hardware resources
  Multiple program running concurrently can be chaotic. It’s the responsibility of the OS to bring order.
    “DESPISE CHAOS, CREATE ORDER”

## Slide 7: ABSTRACTION

## Slide 8: An Extended Machine
Dealing with hardware can be very difficult.
  Need to understand the operation
  Need low level programming
  Consider direct read write to hard disk
Programmers want a simple, high-level abstraction to deal with hardware.
The job of the OS is to create good abstractions
Example:
  OS abstracts hard disk by the file-system

## Slide 9: A Resource Manager
Allows multiple programs to run at the same time
Provide an orderly and controlled allocation of
  Processors
  Memories
  I/0 devices
Among the competing programs
Example:
  3 programs running on some computer
  All tried to print their output simultaneously on the same printer
  The OS can bring order to the potential chaos by buffering all the output on the disk

## Slide 10: A Resource Manager
Resources can be shared in two different ways:
  Time multiplexing:
    In a single CPU system, several running programs take turns.
  Space multiplexing:
    main memory is divided up among several running programs

## Slide 11: Computer Hardware Review

## Slide 12: Processors
Fetches instructions from memory and executes them.
Basic cycle:
  Fetch Decode Execute
The cycle is repeated until the program finishes.

## Slide 13: Pipelining vs Superscalar Architecture

## Slide 14: Multithreaded vs Multicore Chips
Multithreaded Chips
  Replicate some of the control logic.
  Allow the CPU to hold the states of two different threads and then switch back and forth on a nanosecond time scale.
  Does not offer true parallelism though!
Multicore Chips
  CPU chips with two or four or more complete processors or cores on them.
  Requires a multiprocessor operating system.

## Slide 15: Memory
Ideally, a memory should be extremely fast, abundantly large, and dirt cheap.

## Slide 16: Booting the Computer
OS loads every other program into RAM for running
So OS has to load into RAM before any other programs
But how to load the OS into RAM after power-on?
The procedure of starting a computer by loading the OS into RAM is known as booting the system

## Slide 17
Motherboard includes a non-volatile ROM chip
The ROM chip is shipped with a start up program referred to as the BIOS (Basic Input/Output System)
Booting the Computer

## Slide 18
When the computer is booted, BIOS Program is started
BIOS first runs diagnostics to determine the state of the machine
  checks how much RAM is installed and
  checks whether the keyboard and other basic devices are installed and responding correctly
  …
Booting the Computer

## Slide 19
BIOS then determines the boot device by trying a list of devices stored in the CMOS memory
  Hard drive
  CD-ROM
  Flash drive
The first sector from the boot device is read into memory and executed
  This sector contains a program that examines the partition table at the end of the boot sector to determine the active partition
Then a secondary boot loader is read in from that partition.
  This loader reads in the OS from the active partition and starts it.
OS performs the initialization tasks, creates whatever background processes are needed, and starts up a login program or GUI.
Booting the Computer

## Slide 20: Fundamental Concepts

## Slide 21: Kernel
The most fundamental part of an operating system
  Heart of an OS
The first thing that is loaded into memory when OS starts loading
Runs at all times on the computer
Major role includes memory management, process management, disk management etc.
Often used as another name of OS

## Slide 22: Dual-Mode Operation
CPU executes in 2 Modes
  Kernel mode
    CPU can execute all machine instructions
    CPU can use every hardware feature
  User mode
    permits only a subset of the instructions and a subset of the hardware features.
Allows OS to protect itself and other system components

## Slide 23: Dual-Mode Operation
OS runs in kernel mode, user programs in user mode
  OS is Boss, the applications are laborers
Mode bit provided by hardware
  Provides ability to distinguish when system is running user code or kernel code
  Some instructions designated as privileged, only executable in kernel mode

## Slide 24: Kernel Mode Execution
When does CPU start executing in kernel mode?
  System Boot - starting a computer
  Hardware Interrupt - generated by hardware devices to signal that they need some attention from the OS.
  Trap
    A software-generated interrupt caused either by an error (i.e. division by 0 or invalid memory access) or
    By a specific request from a user program that an operating-system service needs to be performed.

## Slide 25: Switching Modes
To obtain services from the operating system,
  an user program must make a system call, which traps into the kernel and invokes the operating system.
The TRAP instruction switches from user mode to kernel mode and starts the operating system.
When the work has been completed, control is returned to the user program at the instruction following the system call.

## Slide 26: System Calls
Programming interface to the services provided by the OS
Typically used from a high-level language (C or C++) program.
Typically a number is associated with each system call, and the OS maintains a table indexed according to these numbers.

## Slide 27: Steps in making a System Call
UNIX has a read system call for reading files
invoked from C programs by calling a library procedure with the same name read like this:
count = read(fd, buffer, nbytes);
See the steps in more details in Section 1.6
TRAP instruction is executed for mode switching

## Slide 28: Trapping into kernel is costly
Save minimal CPU state (PC, sp, …) – done by hardware
Switches to KERNEL mode
KERNEL determines what system call has occurred
KERNEL verifies that the parameters passed are correct and legal
Restore state before returning to user program
User process
System Call
Trap
Mode bit = 0
Save Caller’s state
Execute system call
Restore state
Return
Mode bit = 1
Resume process
User Mode
Mode bit = 1
Kernel Mode
Mode bit = 0

## Slide 29: Examples of Windows & Unix System Calls

## Slide 30: Some OS Components/Services/functions
Process Management
Memory Management
I/O Management
Deadlock Management
File System

## Slide 31: Some UNIX System Calls For Process Management

## Slide 32: The fork()System Call
When fork()is called in process A
  Control is switched to kernel
  Kernel creates new process B which is exact duplicate of process A
  OS now has two identical processes to run. Both resume from after fork().
  return value of fork() will 0 in the child process and will be equal to the child's process identifier (PID) in the parent process

## Slide 33: fork()Example 1

## Slide 34: fork()Example 2
For further practice:
https://www.geeksforgeeks.org/fork-system-call/
https://www.youtube.com/watch?v=IFEFVXvjiHY
What is the output of this code?
Can you draw the fork() tree?

## Slide 35: OS architecture/structure
2 main architectures:
  monolithic kernel
  microkernel

## Slide 37: Monolithic kernel
Entire operating system runs as a single program in kernel mode.
Set of system calls implement all operating system services such as process management, memory management etc.

## Slide 38: Monolithic kernel
Drawbacks:
  increased kernel size
  difficult to understand
  bad maintainability
Advantage
  Good performance

## Slide 39: Microkernel
reduce the kernel to basic process communication and I/O control
let the other system services reside in user space in form of normal processes
user space services are called as servers
  Do most of the work of the operating system.
  One server for managing memory issues
  one server does process management
  another one manages drivers, and so on.

## Slide 40: Microkernel
The main function of the microkernel is to provide a communication facility between the user program and the various servers
if the user program wishes to access a file, it must interact with the file server.
The user program and service communicate indirectly by exchanging messages with the microkernel.

## Slide 41: Microkernel
Drawbacks:
  Performance overhead of user space to kernel space communication
Advantage
  Easier to extend the OS
    All new services are added to user space and consequently do not require modification of the kernel
  More secure & reliable
    most services are running as user processes. If a service fails, the rest of the operating system remains untouched.

## Slide 42: Example
Bugs in the kernel can bring down the system instantly.
What will be the impact of a bug (severe one) in audio driver
  In a Monolithic Kernel based operating system?
  In a Microkernel based operating system?