## Slide 1: Chapter 4
The Processor

## Slide 2: Introduction
CPU performance factors
  Instruction count
    Determined by ISA and compiler
  CPI and Cycle time
    Determined by CPU hardware
We will examine two MIPS implementations
  A simplified version
  A more realistic pipelined version
Simple subset, shows most aspects
  Memory reference: lw, sw
  Arithmetic/logical: add, sub, and, or, slt
  Control transfer: beq, j
§4.1 Introduction

## Slide 3: Instruction Execution
PC → instruction memory, fetch instruction
Register numbers → register file, read registers
Depending on instruction class
  Use ALU to calculate
    Arithmetic result
    Memory address for load/store
    Branch target address
  Access data memory for load/store
  PC ← target address or PC + 4

## Slide 4: CPU Overview

## Slide 5: Multiplexers
Can’t just join wires together
  Use multiplexers

## Slide 6: Control

## Slide 7: Logic Design Basics
§4.2 Logic Design Conventions
Information encoded in binary
  Low voltage = 0, High voltage = 1
  One wire per bit
  Multi-bit data encoded on multi-wire buses
Combinational element
  Operate on data
  Output is a function of input
State (sequential) elements
  Store information

## Slide 8: Combinational Elements
AND-gate
  Y = A & B
A
B
Y
I0
I1
Y
M u x
S
Multiplexer
  Y = S ? I1 : I0
A
B
Y
+
A
B
Y
ALU
F
Adder
  Y = A + B
Arithmetic/Logic Unit
  Y = F(A, B)

## Slide 9: Sequential Elements
Register: stores data in a circuit
  Uses a clock signal to determine when to update the stored value
  Edge-triggered: update when Clk changes from 0 to 1
D
Clk
Q
Clk
D
Q

## Slide 10: Sequential Elements
Register with write control
  Only updates on clock edge when write control input is 1
  Used when stored value is required later
D
Clk
Q
Write
Write
D
Q
Clk

## Slide 11: Clocking Methodology
Combinational logic transforms data during clock cycles
  Between clock edges
  Input from state elements, output to state element
  Longest delay determines clock period

## Slide 12: Building a Datapath
Datapath
  Elements that process data and addresses in the CPU
    Registers, ALUs, mux’s, memories, …
We will build a MIPS datapath incrementally
  Refining the overview design
§4.3 Building a Datapath

## Slide 13: Instruction Fetch
32-bit register
Increment by 4 for next instruction

## Slide 14: Recall: Instruction Formats

## Slide 15: R-Format Instructions
Read two register operands
Perform arithmetic/logical operation
Write register result
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
op | rs | rt | rd | shamt | funct

## Slide 16: Load/Store Instructions
Read register operands
Calculate address using 16-bit offset
  Use ALU, but sign-extend offset
Load: Read memory and update register
Store: Write register value to memory
6 bits | 5 bits | 5 bits | 5+5+6 = 16 bits
op | rs | rt | addr./imm.

## Slide 17: Load/Store Instructions
Read register operands
Calculate address using 16-bit offset
  Use ALU, but sign-extend offset
Load: Read memory and update register
Store: Write register value to memory
6 bits | 5 bits | 5 bits | 5+5+6 = 16 bits
op | rs | rt | addr./imm.
Store
Load

## Slide 18: Branch Instructions
Read register operands
Compare operands
  Use ALU, subtract and check Zero output
Calculate target address
  Sign-extend displacement
  Shift left 2 places (word displacement)
  Add to PC + 4
    Already calculated by instruction fetch

## Slide 19: Branch Instructions
Just re-routes wires
Sign-bit wire replicated

## Slide 20: Composing the Elements
First-cut data path does an instruction in one clock cycle
  Each datapath element can only do one function at a time
  Hence, we need separate instruction and data memories
Use multiplexers where alternate data sources are used for different instructions

## Slide 21: R-Type/Load/Store Datapath

## Slide 22: Full Datapath

## Slide 23: ALU Control
ALU used for
  Load/Store: F = add
  Branch: F = subtract
  R-type: F depends on funct field
§4.4 A Simple Implementation Scheme
ALU control | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | set-on-less-than
1100 | NOR

## Slide 24: ALU Control
Assume 2-bit ALUOp derived from opcode
  Combinational logic derives ALU control
opcode | ALUOp | Operation | funct | ALU function | ALU control
lw | 00 | load word | XXXXXX | add | 0010
sw | 00 | store word | XXXXXX | add | 0010
beq | 01 | branch equal | XXXXXX | subtract | 0110
R-type | 10 | add | 100000 | add | 0010
 |  | subtract | 100010 | subtract | 0110
 |  | AND | 100100 | AND | 0000
 |  | OR | 100101 | OR | 0001
 |  | set-on-less-than | 101010 | set-on-less-than | 0111

## Slide 25: The Main Control Unit
Control signals derived from instruction
0
rs
rt
rd
shamt
funct
31:26
5:0
25:21
20:16
15:11
10:6
35 or 43
rs
rt
address
31:26
25:21
20:16
15:0
4
rs
rt
address
31:26
25:21
20:16
15:0
R-type
Load/ Store
Branch
opcode
always read
read, except for load
write for R-type and load
sign-extend and add

## Slide 26: Datapath With Control

## Slide 27: All Control Signals

## Slide 28: R-Type Instruction

## Slide 29: Load Instruction

## Slide 30: Branch-on-Equal Instruction

## Slide 31: Implementing Jumps
Jump uses word address
Update PC with concatenation of
  Top 4 bits of old PC
  26-bit jump address
  00
Need an extra control signal decoded from opcode
2
address
31:26
25:0
Jump

## Slide 32: Datapath With Jumps Added

## Slide 33: Performance Issues
Longest delay determines clock period
  Critical path: load instruction
  Instruction memory → register file → ALU → data memory → register file
Not feasible to vary period for different instructions
Violates design principle
  Making the common case fast
We will improve performance by pipelining

## Slide 34: Pipelining Analogy
Pipelined laundry: overlapping execution
  Parallelism improves performance
§4.5 An Overview of Pipelining
2 hours
0.5 hour
1.5 hours

## Slide 35: MIPS Pipeline
Five stages, one step per stage
  IF: Instruction fetch from memory
  ID: Instruction decode & register read
  EX: Execute operation or calculate address
  MEM: Access memory operand
  WB: Write result back to register

## Slide 36: MIPS Stages

## Slide 37: Pipeline Performance
Assume time for stages is
  100ps for register read or write
  200ps for other stages
Compare pipelined datapath with single-cycle datapath
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps

## Slide 38: Pipeline Performance
Single-cycle (Tc= 800ps)
Pipelined (Tc= 200ps)
Tc = Time between instructions

## Slide 39: Pipeline Speedup
If all stages are balanced
  i.e., all take the same time
  Time between instructionspipelined = Time between instructionsnonpipelined Number of stages
If not balanced, speedup is less
Speedup due to increased throughput
  Latency (time for each instruction) does not decrease

## Slide 40: Hazards
Situations that prevent starting the next instruction in the next cycle
Structure hazards
  A required resource is busy
Data hazard
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Deciding on control action depends on previous instruction

## Slide 41: Structure Hazards
Conflict for use of a resource
In MIPS pipeline with a single memory
  Load/store requires data access
  Instruction fetch would have to stall for that cycle
    Would cause a pipeline “bubble”
Hence, pipelined datapaths require separate instruction/data memories
  Or separate instruction/data caches

## Slide 42: Data Hazards
An instruction depends on completion of data access by a previous instruction
  add $s0, $t0, $t1 sub $t2, $s0, $t3
$s0 needed here!!!
$s0 written here!!!

## Slide 43: Data Hazards
An instruction depends on completion of data access by a previous instruction
  add $s0, $t0, $t1 sub $t2, $s0, $t3
$s0 needed here!!!
$s0 written here!!!

## Slide 44: Data Hazards
An instruction depends on completion of data access by a previous instruction
  add $s0, $t0, $t1 sub $t2, $s0, $t3
$s0 needed here!!!
$s0 written here!!!

## Slide 45: Data Hazards
An instruction depends on completion of data access by a previous instruction
  add $s0, $t0, $t1 sub $t2, $s0, $t3

## Slide 46: Forwarding (aka Bypassing)
Use result when it is computed
  Don’t wait for it to be stored in a register
  Requires extra connections in the datapath
$s0 needed here!!!
$s0 written here!!!
$s0 ready here!!!
C O M P A R E

## Slide 47: Load-Use Data Hazard
Can’t always avoid stalls by forwarding
  If value not computed when needed
  Can’t forward backward in time!
$s0 needed here!!!
$s0 written here!!!

## Slide 48: Load-Use Data Hazard
Can’t always avoid stalls by forwarding
  If value not computed when needed
  Can’t forward backward in time!
$s0 needed here!!!
$s0 written here!!!
Can we solve by
FORWARDING?
When is the data Ready?
When WAS the data Ready for R-type?

## Slide 49: Load-Use Data Hazard
Can’t always avoid stalls by forwarding
  If value not computed when needed
  Can’t forward backward in time!
$s0 needed here!!!
$s0 written here!!!
Can we solve by
FORWARDING?
When is the data Ready?
When WAS the data Ready for R-type?
Time Travel!!!

## Slide 50: Load-Use Data Hazard
Can’t always avoid stalls by forwarding
  If value not computed when needed
  Can’t forward backward in time!
$s0 needed here!!!
$s0 written here!!!
Can we solve by
FORWARDING?
When is the data Ready?

## Slide 51: Load-Use Data Hazard
Can’t always avoid stalls by forwarding
  If value not computed when needed
  Can’t forward backward in time!

## Slide 52: Code Scheduling to Avoid Stalls
Reorder code to avoid use of load result in the next instruction
C code for A = B + E; C = B + F;
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
stall
stall
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
11 cycles
13 cycles

## Slide 53
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
stall
stall
13 cycles
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13

## Slide 54
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
11 cycles

## Slide 55: Control Hazards
Branch determines flow of control
  Fetching next instruction depends on branch outcome
  Pipeline can’t always fetch correct instruction
    Still working on ID stage of branch
In MIPS pipeline
  Need to compare registers and compute target early in the pipeline
  Add hardware to do it in ID stage

## Slide 56: Branch Scenario
When is the branch decision made?
Branch Taken

## Slide 57: Stall on Branch (Improved)
Assume enough extra hardware to test registers, calculate the branch address, and update the PC during the second stage (ID stage)

## Slide 58: Branch Prediction
Longer pipelines can’t readily determine branch outcome early
  Stall penalty becomes unacceptable
Predict outcome of branch
  Only stall if prediction is wrong
In MIPS pipeline
  Can predict branches not taken
  Fetch instruction after branch, with no delay

## Slide 59: MIPS with Predict Not Taken
Prediction correct
Prediction incorrect

## Slide 60: More-Realistic Branch Prediction
Static branch prediction
  Based on typical branch behavior
  Example: loop and if-statement branches
    Predict backward branches taken
    Predict forward branches not taken
Dynamic branch prediction
  Hardware measures actual branch behavior
    e.g., record recent history of each branch
  Assume future behavior will continue the trend
    When wrong, stall while re-fetching, and update history

## Slide 61: Delayed Branch
Always execute the next sequential instruction
  i.e., taken branch is always delayed
  The delay is hidden by rearrangement
Branch Taken
MIPS Solution to Control Hazard

## Slide 62: Pipeline Summary
Pipelining improves performance by increasing instruction throughput
  Executes multiple instructions in parallel
  Each instruction has the same latency
Subject to hazards
  Structure, data, control
Instruction set design affects complexity of pipeline implementation
The BIG Picture

## Slide 63: MIPS Pipelined Datapath
§4.6 Pipelined Datapath and Control
WB
MEM
Right-to-left flow leads to hazards
Source for
Control Hazard
Source for
data Hazard

## Slide 64: Pipeline registers
Need registers between stages
  To hold information produced in previous cycle
What is the size of the pipeline registers?
32
32
32+32 = 64
32
32
32
32
32x4 = 128
32
32
32
01
32x3 + 1 = 97
32
32
32 +32 = 64
We may need to update the sizes as we proceed!!!

## Slide 65: Pipeline Operation
Cycle-by-cycle flow of instructions through the pipelined datapath
  “Single-clock-cycle” pipeline diagram
    Shows pipeline usage in a single cycle
    Highlight resources used
  c.f. “multi-clock-cycle” diagram
    Graph of operation over time
We’ll look at “single-clock-cycle” diagrams for load & store

## Slide 66: IF for Load

## Slide 67: ID for Load

## Slide 68: EX for Load

## Slide 69: MEM for Load

## Slide 70: WB for Load

## Slide 71: EX for Store

## Slide 72: MEM for Store

## Slide 73: WB for Store

## Slide 74: WB for Load Revisited
Wrong register number

## Slide 75: Corrected Datapath for Load

## Slide 76: Multi-Cycle Pipeline Diagram
Form showing resource usage

## Slide 77: Multi-Cycle Pipeline Diagram
Traditional form

## Slide 78: Single-Cycle Pipeline Diagram
State of pipeline in a given cycle

## Slide 79: Single-Cycle Pipeline Diagram
State of pipeline in a given cycle

## Slide 80: Pipelined Control (Simplified)
EXE Stage
MEM Stage
WB
Stage
IF: No Special Control Needed
ID: No Special Control Needed
Confusing!!!
RegWrite is actually at WB stage

## Slide 81: Pipelined Control
Control signals derived from instruction
  As in single-cycle implementation

## Slide 82: Pipelined Control

## Slide 83: Data Hazards in ALU Instructions
Consider this sequence:
  sub $2, $1,$3 and $12,$2,$5 or $13,$6,$2 add $14,$2,$2 sw $15,100($2)
We can resolve hazards with forwarding
  How do we detect when to forward?
§4.7 Data Hazards: Forwarding vs. Stalling

## Slide 84: Dependencies & Forwarding
IF/ID
ID/EXE
EXE/MEM
MEM/WB
EXE/MEM
EXE/MEM
EXE/MEM
EXE/MEM
IF/ID
IF/ID
IF/ID
IF/ID
ID/EXE
ID/EXE
ID/EXE
ID/EXE
MEM/WB
MEM/WB
MEM/WB
MEM/WB

## Slide 85: Dependencies & Forwarding
$1 has 30
$3 has 50
A read of a register during a clock cycle returns the value written at the end of the first half of the cycle, when such a write occurs
No Potential Hazard
Potential Hazard
Resolved
Via
Forwarding

## Slide 87: Dependencies & Forwarding
$1 has 30
$3 has 50
A read of a register during a clock cycle returns the value written at the end of the first half of the cycle, when such a write occurs
No Potential Hazard
Potential Hazard
Resolved
Via
Forwarding

## Slide 88: Detecting the Need to Forward
Pass register numbers along pipeline
  e.g., ID/EX.RegisterRs = register number for Rs sitting in ID/EX pipeline register
ALU operand register numbers in EX stage are given by
  ID/EX.RegisterRs, ID/EX.RegisterRt
Data hazards when
  1a. EX/MEM.RegisterRd = ID/EX.RegisterRs
  1b. EX/MEM.RegisterRd = ID/EX.RegisterRt
  2a. MEM/WB.RegisterRd = ID/EX.RegisterRs
  2b. MEM/WB.RegisterRd = ID/EX.RegisterRt
Fwd from EX/MEM pipeline reg
Fwd from MEM/WB pipeline reg

## Slide 89: Detecting the Need to Forward
But only if forwarding instruction will write to a register!
  EX/MEM.RegWrite, MEM/WB.RegWrite
And only if Rd for that instruction is not $zero
  EX/MEM.RegisterRd ≠ 0, MEM/WB.RegisterRd ≠ 0

## Slide 90: Forwarding Paths

## Slide 91: Forwarding Paths
EX/MEM.RegisterRd =
ID/EX.RegisterRs
We have not shown regWrite and $zero checks here.

## Slide 92: Forwarding Paths
MEM/WB.RegisterRd =
ID/EX.RegisterRt
We have not shown regWrite and $zero checks here.

## Slide 93: Forwarding Conditions
EX hazard
  if (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRs)) ForwardA = 10
  if (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRt)) ForwardB = 10
MEM hazard
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and (MEM/WB.RegisterRd = ID/EX.RegisterRs)) ForwardA = 01
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and (MEM/WB.RegisterRd = ID/EX.RegisterRt)) ForwardB = 01
00
01
10
00
01
10
MEM/WB
EX/MEM
ID/EX
A
B

## Slide 94: Double Data Hazard
Consider the sequence:
  add $1,$1,$2 add $1,$1,$3 add $1,$1,$4
Both hazards occur
  Want to use the most recent
Revise MEM hazard condition
  Only fwd if EX hazard condition isn’t true

## Slide 95: Double Data Hazard
add $1,$1,$2
add $1,$1,$3
  add $1,$1,$4
MEM/WB
EX/MEM
ID/EX
A
B
CC: cc1 cc2 cc3 cc4 cc5 cc6 cc7
$2: 30 30 30 30 30 30 30
$3: 20 20 20 20 20 20 20
$4: 4 4 4 4 4 4 4
$1: 10 10 10 10 10/40 40/60 60/64
What is
expected?
60 is Forwarded
Earlier value;
WRONG!!!
64 is Forwarded
Correct!!!

## Slide 96: Revised Forwarding Condition
MEM hazard
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and not (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRs)) and (MEM/WB.RegisterRd = ID/EX.RegisterRs)) ForwardA = 01
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and not (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRt)) and (MEM/WB.RegisterRd = ID/EX.RegisterRt)) ForwardB = 01

## Slide 97: Datapath with Forwarding

## Slide 98: Load -> Store (Mem to Mem Copy)
lw $2, 20($1)
sw $2, 15($3)
When is data ready?
When is data needed?

## Slide 99: Load-Use Data Hazard
Need to stall for one cycle
When is data ready?
When is data needed?

## Slide 100: Load-Use Data Hazard
Need to stall for one cycle
How to detect?
Need to detect here
ID/EX
IF/ID
MemRead => lw
rt is the destination register
rt = ID/EX.rt?
rs = ID/EX.rt?

## Slide 101: Load-Use Hazard Detection
Check when using instruction is decoded in ID stage
ALU operand register numbers in ID stage are given by
  IF/ID.RegisterRs, IF/ID.RegisterRt
Load-use hazard when
  ID/EX.MemRead and ((ID/EX.RegisterRt = IF/ID.RegisterRs) or (ID/EX.RegisterRt = IF/ID.RegisterRt))
If detected, stall and insert bubble

## Slide 102: Load-Use Data Hazard
Need to stall for one cycle
How to stall???

## Slide 103: How to Stall
ID/EX.MemRead is asserted
ID/EX.rt = IF/ID.rs = $2
HAZARD!!!
PC
Make all control fields 0.

## Slide 104: How to Stall the Pipeline
Force control values in ID/EX register to 0
  EX, MEM and WB do nop (no-operation)
Prevent update of PC and IF/ID register
  Using instruction is decoded again
  Following instruction is fetched again
  1-cycle stall allows MEM to read data for lw
    Can subsequently forward to EX stage

## Slide 105: Stall/Bubble in the Pipeline
Stall inserted here

## Slide 106: Stall/Bubble in the Pipeline
Or, more accurately…
AND and OR instructions repeat in clock cycle 4 what they did in clock cycle 3:
AND reads registers and decodes, and
OR is refetched from instruction memory.

## Slide 107: Datapath with Hazard Detection
rs and rt
rt
How do we detect?
How to
Stall?
To prevent
Writing on PC
To prevent
Writing on IF/ID

## Slide 108: Stalls and Performance
Stalls reduce performance
  But are required to get correct results
Compiler can arrange code to avoid hazards and stalls
  Requires knowledge of the pipeline structure
The BIG Picture

## Slide 109: Branch Hazards
If branch outcome determined in MEM
§4.8 Control Hazards
PC
Flush these instructions
(Set control values to 0)

## Slide 110: Branch Scenario (RECALLING)
When is the branch decision made?
Branch Taken
How to insert
the bubbles?
Make all control
signals zero
Make the
Instruction zero
Strictly speaking, these
Are not bubbles!

## Slide 111: Reducing Branch Delay
Move hardware to determine outcome to ID stage
  Target address adder
  Register comparator
Example: branch taken
  36: sub $10, $4, $8 40: beq $1, $3, 7 44: and $12, $2, $5 48: or $13, $2, $6 52: add $14, $4, $2 56: slt $15, $6, $7 ... 72: lw $4, 50($7)

## Slide 112: Example: Branch Taken
44:
40:
36:
Puts the bubble
by zeroing the
instruction field
EX  ID

## Slide 113: Example: Branch Taken
72:

## Slide 114: Data Hazards for Branches
PC
Make all
control fields 0.
When is data ready?
When
is data needed?

## Slide 115: Data Hazards for Branches
If a comparison register is a destination of 2nd or 3rd preceding ALU instruction
… <non-dependent>
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
add $4, $5, $6
add $1, $2, $3
beq $1, $4, target
Can resolve using forwarding

## Slide 116: Data Hazards for Branches
beq $1, $4, target
beq stalled
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
When is data ready?
When is data needed?
lw $1, addr
IF
ID
EX
MEM
WB
IF.Flush
All controls
made zero
beq stalled

## Slide 117: Data Hazards for Branches
If a comparison register is a destination of preceding ALU instruction or 2nd preceding load instruction
  Need 1 stall cycle
beq stalled
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
ID
EX
MEM
WB
add $4, $5, $6
lw $1, addr
beq $1, $4, target

## Slide 118: Dynamic Branch Prediction
In deeper and superscalar pipelines, branch penalty is more significant
Use dynamic prediction
  Branch prediction buffer (aka branch history table)
  Indexed by recent branch instruction addresses
  Stores outcome (taken/not taken)
  To execute a branch
    Check table, expect the same outcome
    Start fetching from fall-through or target
    If wrong, flush pipeline and flip prediction

## Slide 119: 1-Bit Predictor: Shortcoming
Consider a loop branch:
  branches nine times in a row
  then is not taken once.
What is the prediction accuracy for this branch, assuming the prediction bit for this branch remains in the prediction buffer?
  Mispredict as taken on last iteration of inner loop
  Then mispredict as not taken on first iteration of inner loop next time around
90% time
Taken
80% time
Accurate

## Slide 120: 2-Bit Predictor
Only change prediction on two successive mispredictions
a branch that strongly favors taken or not taken—as many branches do—will be mispredicted only once.

## Slide 121: Branch Delay Slot
BDS is scheduled with an independent instruction from before the branch.
BDS is scheduled from the target of the branch
BDS may be scheduled from the not-taken fall-through
For (b) & (c):
usually the target instruction will need to be copied because it can be reached by another path.
it must be OK to execute the sub instruction when the branch goes in the unexpected direction.
By “OK” we mean that the work is wasted, but the program will still execute correctly
Best Option

## Slide 122: Calculating the Branch Target
Even with predictor, still need to calculate the target address
  1-cycle penalty for a taken branch
Branch target buffer
  Cache of target addresses
  Indexed by PC when instruction fetched
    If hit and instruction is branch predicted taken, can fetch target immediately

## Slide 123: More on Predicting
correlating predictor: A branch predictor that combines local behavior of a particular branch and global information about the behavior of some recent number of executed branches.
Recent branch Taken?
No
Yes

## Slide 124: More on Predicting
Tournament predictor: A branch predictor with multiple predictions for each branch and a selection mechanism that chooses which predictor to enable for a given branch.

## Slide 125: Exceptions and Interrupts
“Unexpected” events requiring change in flow of control
  Different ISAs use the terms differently
Exception
  Arises within the CPU
    e.g., undefined opcode, overflow, syscall, …
Interrupt
  From an external I/O controller
Dealing with them without sacrificing performance is hard
§4.9 Exceptions

## Slide 126: Handling Exceptions
In MIPS, exceptions managed by a System Control Coprocessor (CP0)
Save PC of offending (or interrupted) instruction
  In MIPS: Exception Program Counter (EPC)
Save indication of the problem
  In MIPS: Cause register
  We’ll assume 1-bit
    0 for undefined opcode, 1 for overflow
Jump to handler at 8000 00180

## Slide 127: An Alternate Mechanism
Vectored Interrupts
  Handler address determined by the cause
Example:
  Undefined opcode: C000 0000
  Overflow: C000 0020
  …: C000 0040
Instructions either
  Deal with the interrupt, or
  Jump to real handler

## Slide 128: Handler Actions
Read cause, and transfer to relevant handler
Determine action required
If restartable
  Take corrective action
  use EPC to return to program
Otherwise
  Terminate program
  Report error using EPC, cause, …

## Slide 129: Exceptions in a Pipeline
Another form of control hazard
Consider overflow on add in EX stage
  add $1, $2, $1
  Prevent $1 from being clobbered
  Complete previous instructions
  Flush add and subsequent instructions
  Set Cause and EPC register values
  Transfer control to handler
Similar to mispredicted branch
  Use much of the same hardware

## Slide 130: Pipeline with Exceptions

## Slide 131: Exception Properties
Restartable exceptions
  Pipeline can flush the instruction
  Handler executes, then returns to the instruction
    Refetched and executed from scratch
PC saved in EPC register
  Identifies causing instruction
  Actually PC + 4 is saved
    Handler must adjust

## Slide 132: Datapath with controls to handle exceptions

## Slide 133: Exception Example
Exception on add in
  40 sub $11, $2, $4 44 and $12, $2, $5 48 or $13, $2, $6 4C add $1, $2, $1 50 slt $15, $6, $7 54 lw $16, 50($7) …
Handler
  80000180 sw $25, 1000($0) 80000184 sw $26, 1004($0) …

## Slide 134: Exception Example
4c
48
44
50
54

## Slide 135: Exception Example

## Slide 136: Multiple Exceptions
Pipelining overlaps multiple instructions
  Could have multiple exceptions at once
Simple approach: deal with exception from earliest instruction
  Flush subsequent instructions
  “Precise” exceptions
In complex pipelines
  Multiple instructions issued per cycle
  Out-of-order completion
  Maintaining precise exceptions is difficult!

## Slide 137: Imprecise Exceptions
Just stop pipeline and save state
  Including exception cause(s)
Let the handler work out
  Which instruction(s) had exceptions
  Which to complete or flush
    May require “manual” completion
Simplifies hardware, but more complex handler software
Not feasible for complex multiple-issue out-of-order pipelines

## Slide 138: EPC: Precise vs. Imprecise
4c
48
44
50
54
4C + 4
= 50h
e.g., 58

## Slide 139: Instruction-Level Parallelism (ILP)
Pipelining: executing multiple instructions in parallel
To increase ILP
  Deeper pipeline
    Less work per stage ⇒ shorter clock cycle
  Multiple issue
    Replicate pipeline stages ⇒ multiple pipelines
    Start multiple instructions per clock cycle
    CPI < 1, so use Instructions Per Cycle (IPC)
    E.g., 4GHz 4-way multiple-issue
      16 BIPS, peak CPI = 0.25, peak IPC = 4
    But dependencies reduce this in practice
§4.10 Parallelism via Instructions

## Slide 140: Multiple Issue
Static multiple issue
  Compiler groups instructions to be issued together
  Packages them into “issue slots”
  Compiler detects and avoids hazards
Dynamic multiple issue
  CPU examines instruction stream and chooses instructions to issue each cycle
  Compiler can help by reordering instructions
  CPU resolves hazards using advanced techniques at runtime

## Slide 141: Speculation
“Guess” what to do with an instruction
  Start operation as soon as possible
  Check whether guess was right
    If so, complete the operation
    If not, roll-back and do the right thing
Common to static and dynamic multiple issue
Examples
  Speculate on branch outcome
    Roll back if path taken is different
  Speculate on load followed by a store (whether the load is dependent on the store)
    Roll back if location is updated

## Slide 142: Compiler/Hardware Speculation
Compiler can reorder instructions
  e.g., move load before branch
  Can include “fix-up” instructions to recover from incorrect guess
Hardware can look ahead for instructions to execute
  Buffer results until it determines they are actually needed
  Flush buffers on incorrect speculation

## Slide 143: Speculation and Exceptions
What if exception occurs on a speculatively executed instruction?
  e.g., speculative load before null-pointer check
Static speculation
  Can add ISA support for ignoring exceptions until it is clear that they really should occur
Dynamic speculation
  Can buffer exceptions until instruction completion
    i.e., the instruction is not speculative anymore

## Slide 144: Static Multiple Issue
Compiler groups instructions into “issue packets”
  Group of instructions that can be issued on a single cycle
  Determined by pipeline resources required
Think of an issue packet as a very long instruction
  Specifies multiple concurrent operations
  ⇒ Very Long Instruction Word (VLIW)

## Slide 145: Scheduling Static Multiple Issue
Compiler must remove/reduce/prevent some/all hazards
  Reorder instructions into issue packets
  No dependencies within a packet
  Possibly some dependencies between packets
    This will be handled by Hardware (forwarding/Stall)
  Pad with nop if necessary

## Slide 146: MIPS with Static Dual Issue
Two-issue packets
  One ALU/branch instruction
  One load/store instruction
  64-bit aligned
    ALU/branch, then load/store
    Pad an unused instruction with nop
Address | Instruction type | Pipeline Stages |  |  |  |  |  | 
n | ALU/branch | IF | ID | EX | MEM | WB |  | 
n + 4 | Load/store | IF | ID | EX | MEM | WB |  | 
n + 8 | ALU/branch |  | IF | ID | EX | MEM | WB | 
n + 12 | Load/store |  | IF | ID | EX | MEM | WB | 
n + 16 | ALU/branch |  |  | IF | ID | EX | MEM | WB
n + 20 | Load/store |  |  | IF | ID | EX | MEM | WB

## Slide 147: MIPS with Static Dual Issue
3 NEW
Reg.
Addr. ports;
2 for read
1 for write
2 new
read
ports
New write
port

## Slide 148: Hazards in the Dual-Issue MIPS
More instructions executing in parallel
EX data hazard
  Forwarding avoided stalls with single-issue
  Now can’t use ALU result in load/store in same packet
    add $t0, $s0, $s1 load $s2, 0($t0)
    Split into two packets, effectively a stall
Load-use hazard
  (between two issue packet)
  Still one cycle use latency, but now two instructions
More aggressive scheduling required

## Slide 149: Scheduling Example
Schedule this for dual-issue MIPS
Loop: lw $t0, 0($s1) # $t0=array element addu $t0, $t0, $s2 # add scalar in $s2 sw $t0, 0($s1) # store result addi $s1, $s1,–4 # decrement pointer bne $s1, $zero, Loop # branch $s1!=0
 | ALU/branch | Load/store | cycle
Loop: | nop | lw $t0, 0($s1) | 1
 | addi $s1, $s1,–4 | nop | 2
 | addu $t0, $t0, $s2 | nop | 3
 | bne $s1, $zero, Loop | sw $t0, 4($s1) | 4
  IPC = 5/4 = 1.25 (c.f. peak IPC = 2)

## Slide 150: Loop Unrolling
Replicate loop body to expose more parallelism
  Reduces loop-control overhead
Use different registers per replication
  Called “register renaming”
  Avoid loop-carried “anti-dependencies”
    Store followed by a load of the same register
    Aka “name dependence”
      Reuse of a register name

## Slide 151: Loop Unrolling Example
IPC = 14/8 = 1.75
  Closer to 2, but at cost of registers and code size
 | ALU/branch | Load/store | cycle
Loop: | addi $s1, $s1,–16 | lw $t0, 0($s1) | 1
 | nop | lw $t1, 12($s1) | 2
 | addu $t0, $t0, $s2 | lw $t2, 8($s1) | 3
 | addu $t1, $t1, $s2 | lw $t3, 4($s1) | 4
 | addu $t2, $t2, $s2 | sw $t0, 16($s1) | 5
 | addu $t3, $t4, $s2 | sw $t1, 12($s1) | 6
 | nop | sw $t2, 8($s1) | 7
 | bne $s1, $zero, Loop | sw $t3, 4($s1) | 8
Loop: lw $t0, 0($s1) addu $t0, $t0, $s2 sw $t0, 0($s1) addi $s1, $s1,–4 bne $s1, $zero, Loop

## Slide 152: Dynamic Multiple Issue
“Superscalar” processors
CPU decides whether to issue 0, 1, 2, … each cycle
  Avoiding structural and data hazards
Avoids the need for compiler scheduling
  Though it may still help

## Slide 153: Simple superscalar vs. VLIW
The code is guaranteed by the hardware to execute correctly.
  independent of the issue rate
  or pipeline structure of the processor.
In VLIW, recompilation may be required for different processor models;
In other static issue processors, code should run correctly across different implementations
  but often so poorly as to make compilation effectively required.

## Slide 154: Dynamic Pipeline Scheduling
Allow the CPU to execute instructions out of order to avoid stalls
  But commit result to registers in order
Example
  lw $t0, 20($s2) addu $t1, $t0, $t2 sub $s4, $s4, $t3 slti $t5, $s4, 20
  Can start sub while addu is waiting for lw

## Slide 155: Dynamically Scheduled CPU
Results also sent to any waiting reservation stations
Reorders buffer for register writes
Can supply operands for issued instructions
Preserves dependencies
Hold pending operands

## Slide 156: Register Renaming
Reservation stations and reorder buffer effectively provide register renaming
On instruction issue to reservation station
  If operand is available in register file or reorder buffer
    Copied to reservation station
    No longer required in the register; can be overwritten
  If operand is not yet available
    It will be provided to the reservation station by a function unit
      The name of the functional unit is tracked
    Register update may not be required

## Slide 157: Speculation
Predict branch and continue issuing
  Don’t commit until branch outcome determined
Load speculation
  support speculation on load addresses,
  allowing load-store reordering,
  Don’t commit load until speculation cleared

## Slide 158: Why Do Dynamic Scheduling?
Why not just let the compiler schedule code?
Not all stalls are predicable
  e.g., cache misses
Can’t always schedule around branches
  Branch outcome is dynamically determined
Different implementations of an ISA have different latencies and hazards

## Slide 159: Does Multiple Issue Work?
Yes, but not as much as we’d like
Programs have real dependencies that limit ILP
Some dependencies are hard to eliminate
Some parallelism is hard to expose
Memory delays and limited bandwidth
  Hard to keep pipelines full
Speculation can help if done well
The BIG Picture

## Slide 160: ARM Cortex-A8 Pipeline
Address
Generation
Unit
Branch Target Buffer
Global History Buffer
Return Stack

## Slide 161: Concluding Remarks
ISA influences design of datapath and control
Datapath and control influence design of ISA
Pipelining improves instruction throughput using parallelism
  More instructions completed per second
  Latency for each instruction not reduced
Hazards: structural, data, control
Multiple issue and dynamic scheduling (ILP)
  Dependencies limit achievable parallelism
  Complexity leads to the power wall
§4.14 Concluding Remarks